R-27ST

SERVICE MANUAL

S6216R27STPHS

KG     PCS

1

MICRO-ONDES

AUTO COOK

2

3

EXPRESS COOK

EXPRESS DEFROST

kg

MODELE

R-27ST

In the interests of user-safety the oven should be restored to its original condition and only parts identical to those specified should be used.

SOMMAIRE

SOMMAIRE

CHAPITRE 1. AVANT L’ENTRETIEN

CHAPITRE 9. PANNEAU DE COMMANDE-CLAVIER

CHAPITRE 2. MISE EN GARDE POUR LES TECHNICIENS

CHAPITRE 3.  SPECIFICATIONS DU PRODUIT CHAPITRE 4. VUE APPARENTE

CHAPITRE 5. SEQUENCE DE FONCTIONNEMENT

CHAPITRE 6. FONCTIONS DES COMPOSANTS IMPORTANTS

CHAPITRE 7. GUIDE DE DEPANNAGE GUIDE CHAPITRE 8.  PROCEDURES DE TEST

CHAPITRE 10. PRECAU TIONS D’UTILISATION DE LA SOUDURE SANS PLOMB

CHAPITRE 11. TEMPLACEMENT DE COMPOSANTS ET PROCEDURE DE REGLAGES

CHAPITER 12. MESURE DE  MICRO-ONDES CHAPITRE 13. SCHEMAS ELECTRIQUES

Guide des pièces détachées

This document has been published to be used for after sales service only.

The contents are subject to change without notice.

SOMMAIRES

CHAPITRE 1. AVANT L’ENTRETIEN

[1]INFORMATION GENERALE IMPORTANTE... .................................................. 1-1

[2]   MISE EN GARDE SUR LES

MICRO-ONDES.……………………………………..…………..1-1

[3]    WARNING .................................................... 1-1

CHAPITRE 2. AVERTISSEMENT AUX TECHNICIENS

CHAPITRE 3. SPECIFICATIONS DU PRODUIT CHAPITRE 4. VUE APPARENTE

[1]    FOUR......................................................... 4-1

[2]    CLAVIER…………………........................ 4-1

CHAPITRE 5. OPERATION SEQUENCE

[1]	MODE ARRET............................................. 5-1

[2]CONDITION DE CUISSON AU MICRO-ONDES...... 5-1 [3]	 POWER OUTPUT REDUCTION ................ 5-1

CHAPITRE 6. FONCTION IMPORTANTE DES COMPOSANTS

[1]	DOOR OPEN MECHANISM ...................... 6-1 [2]	SECONDARY INTERLOCK SWITCH........ 6-1 [3]	DOOR SENSING SWITCH ........................ 6-1 [4]	MONITOR SWITCH ................................... 6-1 [5]	FUSE T6.3A ............................................... 6-1 [6]	TEMPERATURE FUSE 150C (OVEN) ...... 6-1 [7]	ASYMMETRIC RECTIFIER ....................... 6-1 [8]	TURNTABLE MOTOR................................ 6-1 [9]	FAN MOTOR.............................................. 6-1 [10]  NOISE FILTER........................................... 6-1 [11] HIGH VOLTAGE FUSE.......................... ..... 6-1

CHAPTER 7. TROUBLESHOOTING GUIDE CHAPTER 8. TEST PROCEDURES

[1]    A: MAGNETRON TEST ............................. 8-1

[2]    B: HIGH VOLTAGE TRANSFORMER

TEST .......................................................... 8-1 [3]    C: HIGH VOLTAGE RECTIFIER TEST ...... 8-2 [4]    D: HIGH VOLTAGE CAPACITOR TEST..... 8-2 [5]    E: SWITCH TEST ...................................... 8-2 [6]    F: TEMPERATURE FUSE TEST ............... 8-2 [7]    G: MOTOR WINDING TEST...................... 8-3 [8]    H: FUSE T6.3A .......................................... 8-3 [9]    I: NOISE FILTER TEST ............................. 8-3 [10] Procedure J: HIGH VOLTAGE FUSE

TEST ................................................................. 8-3

[11] Procedure K: TOUCH CONTROL PANEL ASSEMBLY TEST ............................................. 8-3 [12] Procedure L: SWITCH UNIT TEST ............ 8-4 [13] Procedure M: RELAY TEST ................... ... 8-4 [14] Procedure N: PROCEDURES TO

THE CONTROL UNIT........................................ 8-4

CHAPTER 9. TOUCH CONTROL PANEL ASSEM- BLY

[1]    OUTLINE OF TOUCH CONTROL PAN-

EL .............................................................. 9-1 [2]    SERVICING FOR TOUCH CONTROL

PANEL ....................................................... 9-1

CHAPTER 10. PRECAUTIONS FOR USING LEAD- FREE SOLDER

CHAPTER 11. COMPONENT REPLACEMENT AND ADJUSTMENT PROCEDURE

[1]	BEFORE OPERATING .............................11-1 [2]	OUTER CASE REMOVAL ........................11-1 [3]	HIGH VOLTAGE TRANSFORMER RE-

MOVAL......................................................11-2 [4]    HIGH VOLTAGE RECTIFIER ASSEM-

BLY AND HIGH VOLTAGE CAPACITOR REMOVAL.................................................11-2

[5]	MAGNETRON REMOVAL ........................11-2 [6]	POSITIVE LOCK CONNECTOR (NO-

CASE TYPE) REMOVAL ..........................11-2 [7]    TURNTABLE MOTOR REMOVAL ............11-2 [8]    COOLING FAN MOTOR REMOVAL .........11-3 [9]    POWER SUPPLY CORD REPLACE-

MENT ........................................................11-4 [10]  CONTROL PANEL ASSEMBLY RE-

MOVAL......................................................11-4 [11]  SECONDARY INTERLOCK SWITCH,

DOOR SENSING SWITCH AND MONI-

TOR SWITCH REMOVAL .........................11-4 [12]  SECONDARY INTERLOCK SWITCH,

DOOR SENSING SWITCH AND MONI-

TOR SWITCH ADJUSTMENT ..................11-4 [13]  DOOR REPLACEMENT ...........................11-5

CHAPTER 12. MICROWAVE MEASUREMENT CHAPTER 13. CIRCUIT DIAGRAMS

[1]    Oven Schematic....................................... 13-1

[2]    Pictorial Diagram (Figure S-1) ................. 13-3 [3]    Control Unit Circuit (Figure S-2)............... 13-4 [4]    Printed Wiring Board ............................... 13-5

Parts List

[1] GENERAL IMPORTANT INFORMATION

This Manual has been prepared to provide Sharp Corp. Service engineers with Operation and Service Information.

It is recommended that service engineers carefully study the entire text of this manual, so they will be qualified to render satisfactory customer ser- vice.

WARNING: THIS APPLIANCE MUST BE EARTHED

IMPORTANT

THE WIRES IN THIS MAINS LEAD ARE COLOURED IN ACCORDANCE WITH THE FOLLOWING CODE: GREEN-AND-YELLOW--------------EARTH

BLUE---------------------------------NEUTRAL BROWN-------------------------------------LIVE

[2] CAUTION MICROWAVE RADIATION

DO NOT BECOME EXPOSED TO RADIATION FROM THE MICROWAVE GENERATOR OR OTHER PARTS CON- DUCTING MICROWAVE ENERGY.

Service engineers should not be exposed to the microwave energy which may radiate from the magnetron or other microwave generating devices if it is improperly used or connected. All input and output microwave connections, waveguides, flanges and gaskets must be secured. Never operate the device without a microwave energy absorbing load attached. Never look into an open waveguide or antenna while the device is energized.

[3] WARNING

Never operate the oven until the following points are ensured. (A) The door is tightly closed.

(B) The door brackets and hinges are not defective. (C) The door packing is not damaged.

(D) The door is not deformed or warped.

(E) There is not any other visible damage with the oven.

Servicing and repair work must be carried out only by trained service engineers. All the parts marked "	" on parts list are used at voltages more than 250V. Removal of the outer wrap gives access to potentials above 250V.

All the parts marked "*" on parts list may cause undue microwave exposure, by themselves, or when they are damaged,

loosened or removed.

CHAPITRE 2. MISE EN GARDE POUR LE PERSONNEL TECHNIQUE

Microwave ovens contain circuitry capable of producing very high voltage and current, contact with any part of the high voltage circuit will result in electrocution. High voltage capacitor, Power transformer, Magnetron, High voltage rectifier assembly, High voltage harness, High voltage fuse.

REMEMBER TO CHECK 3D

1) Disconnect the supply.

2) Door opened, and wedged open.

3) Discharge the high voltage capacitor.

WARNING: AGAINST  THE  CHARGE  OF  THE  HIGH-VOLTAGE CAPACITOR

The high-voltage capacitor remains charged about 60 sec- onds after the oven has been switched off. Wait for 60 sec- onds and then short-circuit the connection of the high- voltage capacitor (that is, of the connecting lead of the high-voltage rectifier) against the chassis with the use of an insulated screwdriver.

Sharp recommend that wherever possible fault-finding is carried out with the supply disconnected. It may, in some cases, be necessary to connect the supply after the outer case has been removed, in this event carry out 3D checks and then disconnect the leads to the pri- mary of the power transformer. Ensure that these leads remain iso- lated from other components and the oven chassis. (Use insulation tape if necessary.) When the testing is completed, carry out 3D checks and reconnect the leads to the primary of the power transformer.

REMEMBER TO CHECK 4R

1) Reconnect all leads removed from components during testing.

2) Replace the outer case (cabinet).

3) Reconnect the supply.

4) Run the oven. Check all functions.

Microwave ovens should not be run empty. To test for the presence of microwave energy within a cavity, place a cup of cold water on the oven  turntable, close  the  door  and  set  the  power  level  to  HIGH (100%). And set the microwave timer for two (2) minutes. When the two minutes has elapsed (timer at zero) carefully check that the water is now hot. If the water remains cold, carry out 3D checks and re- examine the connections to the component being tested.

When all service work is completed and the oven is fully assembled, the microwave power output should be checked and microwave leakage test should be carried out.

| ITEM | DESCRIPTION |
| --- | --- |
| Power Requirements | 230 Volts 50 Hertz Single phase, 3 wire earthed |
| Consommation électrique | 1.25 kW Less than 0.5W at OFF mode (Energy Save Mode) |
| Puissance de sortie | 800 watts nominal of RF microwave energy (IEC60705 Test Procedure) Operating frequency 2450 MHz |
| Dimensions Extérieures | Width 460 mm Height 275 mm including foot Depth 380 mm |
| Dimensions de la cavité du four | Width 319 mm NOTE: Internal capacity is calculated by measuring maximum width, depth and height. Height 211 mm Actual capacity for holding food is less. Depth 336 mm |
| Diamètre du plateau tournant | 272 mm |
| Fonctions de contrôle complémentaire | Touch Control System Timer (0 - 99 minutes 90 seconds) Microwave Power for Variable Cooking Repetition Rate; 100P ....................................................... Full power throughout the cooking time 70P .........................................................approx. 70% of FULL Power 50P ....................................................... approx. 50% of FULL Power 30P ........................................................approx. 30% of FULL Power 10P .........................................................approx. 10% of FULL Power AUTO COOK button EXPRESS COOK button EXPRESS DEFROST button POWER LEVEL button STOP/CLEAR button START/AUTO MINUTE button TIME/WEIGHT knob |
| Poids (Approx.) | 12 kg |

CHAPITRE 4. VUE APPARENTE

[1] FOUR

1. Door opening handle

2. Oven lamp

3. Door hinges

4. Door safety latches

5. Door

6. Door seals and sealing surfaces

6 	2

1 	3

9 	11

7. Coupling

9. Control panel

10. Waveguide cover	4

11. Power supply cord

12. Ventilation openings

13. Outer case cabinet

14. Turntable

15. Roller stay

[2] PANNEAU DE CONTROLE

T

1. DIGITAL DISPLAY

2. INDICATORS BUTTONS:

3. AUTO COOK

4. EXPRESS COOK

5. EXPRESS DEFROST

6. START/AUTO MINUTE

7. STOP/CLEAR

8. POWER LEVEL

9. TIME/WEIGHT KNOB

8 	7 	10 4

5

14

15

13

12

1

KG     PCS	2

AUTO COOK

1	3

2

3

EXPRESS COOK

4

EXPRESS DEFROST

5

6

7

8

kg	9

[1] OFF CONDITION

1.  When the oven is plugged in with the door closed, the line voltage is supplied to the noise filter. And the display shows nothing.

2.  When the door is opened with plugged in, the contacts (COM-NC) of the secondary interlock switch is closed. And the line voltage is supplied to the T/C transformer of the control unit. Then the con- tacts of the relay RY-6 are closed. And the contacts of the relay RY-

5 are closed and the oven lamp is turned on. The display shows “

.0”.

3.  When the door is closed, the contacts (COM-NC) of the secondary interlock switch are opened. Because the contacts of the relay RY-6 have been closed, the line voltage is kept supplying to the T/C transformer of the control unit. But the contacts of the relay RY-5 are opened and the oven lamp is turned off.

NOTE: Energy save mode

1) If the oven has not been used for 3 minutes or more, the contacts of the relay RY-6 will be opened and the control unit will not be energized. Open and close the door, the control unit will resume.

IMPORTANT

When the oven door is closed, the monitor switch contacts (COM-NC)

must be open.

[2] MICROWAVE COOKING CONDITION

1. HIGH COOKING

Enter a desired cooking time by rotating the TIME/WEIGHT knob and start the oven with pressing START button.

The circuits to the high voltage transformer, fan motor, turntable motor are cut off when the secondary interlock switch and door sensing switch are made open. The oven lamp is turned on.

6.  MONITOR SWITCH CIRCUIT

The monitor switch is mechanically controlled by oven door, and monitors the operation of the secondary interlock switch, the relay (RY1) and the primary interlock relay.

1) When the oven door is opened during or after the cycle of a cooking program, the secondary interlock switch and door sens- ing switch must open their contacts first. After that the contacts (COM-NC) of the monitor switch can be closed.

2) When the oven door is closed, the contacts (COM-NC) of the monitor switch must be opened. After that the contacts of the secondary interlock switch and door sensing switch are closed.

3) When the oven door is opened and the contacts of the second- ary interlock switch and the primary interlock relay (RY2) remain closed. The fuse T6.3A will blow, because the monitor switch is closed and a short circuit is caused.

2. MEDIUM HIGH, MEDIUM, MEDIUM LOW, LOW COOKING

When the microwave oven is preset for variable cooking power, rated voltage is supplied to the high voltage transformer intermittently within a 32-second time base through the relay contact which is coupled with the  current-limiting relay  RY2.  The  following  levels  of  microwave power are given.

SETTING;

32 sec. ON

Function sequence

Figure O-2 on page 14-1

100P (HIGH)

70P (MEDIUM

24 sec. ON 	8 sec. OFF

100%

HIGH)	Approx. 70%

CONNECTED COMPONENTS	RELAY

Oven lamp, Fan motor, Turntable motor	RY5 high voltage transformer	RY2

50P (MEDIUM)

30P (MEDIUM

18 sec. ON

12 sec. ON

14 sec. OFF

20 sec. OFF

Approx. 50%

1.  Rated voltage is supplied to the primary winding of the high voltage

LOW)	Approx. 30%

transformer. The voltage is converted to about 3.3 volts A.C. output on the filament winding and high voltage of approximately 2000 volts A.C. on the secondary winding.

10P (LOW)

6 sec. ON

26 sec. OFF

Approx. 10%

2.  The filament winding voltage (3.3 volts) heats the magnetron fila- ment and the high voltage (2000 volts) is sent to the voltage dou- bling circuit, where it is doubled to negative voltage of approximately 4000 volts D.C..

3.  The 2450 MHz microwave energy produced in the magnetron gen- erates a wave length of 12.24cm. This energy is channelled through the waveguide (transport channel) into the oven cavity, where the food is placed to be cooked.

4.  When the cooking time is up, a signal tone is heard and the relays (RY5+RY2) go back to their home position. The circuits to the oven lamp, high voltage transformer, fan motor and turntable motor are cut off.

5.  When the door is opened during a cook cycle, the switches come to the following condition

NOTE: The ON/OFF time ratio does not exactly correspond to the percentage of microwave power, because approx. 3 seconds are needed for heating up the magnetron filament.

[3] POWER OUTPUT REDUCTION

After 100% power cooking mode is carried out for more than 20 min- utes, the power out-put is automatically reduced to 70%. Even if the cooking time is shorter than for 20 minutes, the power output is reduced to 70% after total cooking time over 20 minutes when the oven is started in 100% power cooking mode again within 1 minute and 35 seconds.

SWITCH	CONTACT		DURING COOKING

CONDITION DOOR OPEN (NO COOKING)

Secondary interlock switch

COM-NO	Closed	Open

COM-NC	Open	Closed

Door sensing switch	COM-NO	Closed	Open

Monitor switch	COM-NC	Open	Closed

CHAPTER 6. FONCTION DES COMPOSANTS IMPORTANTS

[1] DOOR OPEN MECHANISM

The door is opened by pulling the door, refer to the Figure D-1.

Latch Heads

Latch Hook

Door Sensing Switch

Monitor Switch

Door

[6] TEMPERATURE FUSIBLE 150°C (FOUR)

The temperature fuse ocated on the top of the oven cavity is designed to prevent damage to the oven if the foods in the oven catch fire due to over heating produced by improper setting of cook time or failure of control unit. Under normal operation, the temperature fuse remains closed. However, when abnormally high temperatures are reached within the oven cavity, the temperature fuse will open at 150°C, caus- ing the oven to shut down. The defective temperature fuse must be replaced with a new one.

[7] ASYMMETRIC RECTIFIER

The asymmetric rectifier is solid state device that prevents current flow in both directions. And it prevents the temperature rise of the high volt- age transformer by blowing the fuse T6.3A when the high voltage rec- tifier is shorted.

Secondary interlock Switch

Figure D-1. Door Open Mechanism

[2] SECONDARY INTERLOCK SWITCH

1.  When the oven door is closed, the contacts (COM-NO) of the switch must be closed. And the contacts (COMNC) must be opened.

2.  When the oven door is opened, the contacts (COMNO) of the switch must be opened. And the contacts (COM-NC) must be closed.

[3] DOOR SENSING SWITCH

1.  When the oven door is closed, the contacts (COM-NO) must be closed.

2.  When the oven door is opened, the contacts (COM-NO) must be opened.

[4] MONITOR SWITCH

1.  When the oven door is closed, the contacts (COM-NC) must be opened.

2.  When the oven door is opened, the contacts (COM-NC) must be closed.

3.  If the oven door is opened and the contacts (COM-NO) of the sec- ondary interlock switch and the primary interlock relay (RY2) fail to open, the fuse T6.3A blows simultaneously with closing the con- tacts (COM-NC) of the monitor switch.

CAUTION: BEFORE REPLACING A FUSE T6.3A TEST THE SEC- ONDARY INTERLOCK SWITCH AND PRIMARY INTER- LOCK RELAY (RY2) AND MONITOR SWITCH   FOR PROPER OPERATION. (REFER TO CHAPTER “TEST PROCEDURE”.)

[5] FUSIBLE T6.3A

1.  The fuse T6.3A blows when the contacts (COM-NO) of the second- ary interlock switch and the primary interlock relay (RY2) remain closed with the oven door open and when the monitor switch closes.

2.  If the wire harness or electrical components are short-circuited, the fuse T6.3A blows to prevent an electric shock of fire hazard.

D2	D1

ASYMMETRIC

RECTIFIER	HIGH VOLTAGE RECTIFIER

The rated peak reverse voltage of D1 of the asymmetric rectifier is 6

KV The rated peak reverse voltage of D2 of the asymmetric rectifier is

1.7 KV. D1 and D2 of the asymmetric rectifier or high voltage rectifier are shorted when the each peak reverse voltage goes beyond the each rated peak reverse voltage. (The process of the blowing the fuse T6.3A.)

1.  The high voltage rectifier is shorted by some fault when microwave cooking or dual cooking.

2.  The peak reverse voltage of D2 of the rectifier goes beyond the rated peak reverse voltage 1.7 KV in the voltage doubler circuit.

3.  D2 of the rectifier is shorted.

4.  The large electric currents flow through the high voltage winding of the high voltage transformer.

5.  The large electric currents beyond 6.3A flow through the primary winding of the high voltage transformer.

6.  The fuse T6.3A blows by the large electric currents.

7.  The power supplying to the high voltage transformer is cut off.

[8]  PLATEAU TOURNANT

The turntable motor drives the turntable roller assembly to rotate the turntable.

[9] MOTEUR VENTILATEUR

The fan motor drives a blade which draws external cool air. This cool air is directed through the air vanes surrounding the magnetron and cools the magnetron. This air is channelled through the oven cavity to remove steam and vapours given off from the heating foods. It is then exhausted through the exhausting air vents at the oven cavity.

[10] FILTRE SECTEUR

The noise filter prevents the radio frequency interference that might flow back in the power circuit.

[11] FUSIBLE HAUTE TENSION

The high voltage fuse blows when the high voltage rectifier or the magnetron is shorted.

CHAPTER 7. TROUBLESHOOTING GUIDE

When troubleshooting the microwave oven, it is helpful to follow the Sequence of Operation in performing the checks. Many of the possible causes of trouble will require that a specific test be performed. These tests are given a procedure letter which will be found in the "Test Pro- cedure"section.

IMPORTANT:

If the oven becomes inoperative because of a blown fuse T6.3A in the secondary interlock switch - primary interlock relay (RY2) - monitor switch circuit, check the secondary interlock switch, primary interlock relay (RY2) and monitor switch before replacing the fuse T6.3A.

| TEST PROCEDURE | A | B | C | CK | D | E | E | E | F | G | G | H | K | M | M | N | RE | CK | CK | RE | CK | CK | CK | CK | CK | I | L | J |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CONDITION | POSSIBLE CAUSE AND DEFECTIVE PARTS PROBLEM | MAGNETRON | HIGH VOLTAGE TRANSFORMER | H.V. RECTIFIER ASSEMBLY | HIGH VOLTAGE WIRE | HIGH VOLTAGE CAPACITOR | 1ST. LATCH SWITCH | 2ND. INTERLOCK RELAY CONTROL SWITCH | MONITOR SWITCH | TEMPERATURE FUSE 150ºC (OVEN) | FAN MOTOR | TURNTABLE MOTOR | FUSE T6.3A | TOUCH CONTROL PANEL | RELAY (RY-1) | RELAY (RY-2) | FOIL PATERN ON P.W.B. | POWER SUPPLY CORD | SHORTED WIRE HARNESS | OPENED WIRE HARNESS | OVEN LAMP | WALL OUTLET | MISADJUSTMENT SWITCH | HOME FUSE OR BREAKER | BLOCKED COOLING FAN | BLOCKED VENTILATION | NOISE FILTER | SWITCH UNIT | H.V. FUSE |
| OFF CONDITION | Home fuse blows when pow- ersupply cord is plugged into wall outlet. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | FUSE T6.3A blows when power supply cord is plug- ged into wall outlet. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | "88:88" does not appear in display but power supply cord is plugged into wall outlet. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Display does not operate properly when STOP/CLEAR button is pressed. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ON CONDITION | Oven does not start when the START button is touched. (Display appears) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Oven lamp does not light (Display appears.) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Fan motor does not operate. (Display appears.) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Turntable motor does not operate. (Display appears.) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Oven or any electrical parts does not stop when cooking time is 0 or STOP button is pressed. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Oven seems to be operating but little or no heat is pro- duced in oven load. (Micro- wave power level is set at 100%) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Oven does not seems to be operating properly when 70%,50%, 30% or 10% is set. (Oven operates properly at 100%.) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Oven goes into cook cycle bu tshuts down before end of cooking cycle. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

CHAPTER 8. TEST PROCEDURES

[1] A: MAGNETRON TEST

NEVER TOUCH ANY PART IN THE CIRCUIT WITH YOUR HAND OR AN INSULATED TOOL WHILE THE OVEN IS IN OPERATION.

1.  CARRY OUT 3D CHECKS.

2.  To test for an open filament, isolate the magnetron from the high voltage circuit. A continuity check across the magnetron filament leads should indicate less than 1 ohm.

3.  To test for a shorted magnetron, connect the ohmmeter leads between the magnetron filament leads and chassis ground. This test should indicate an infinite resistance. If there is little or no resistance the magnetron is grounded and must be replaced.

4.  Reconnect all leads removed from components during testing.

5.  Reinstall the outer case (cabinet).

6.  Reconnect the power supply cord after the outer case is installed.

7.  Run the oven and check all functions.

1. MICROWAVE OUTPUT POWER

The following test procedure should be carried out with the microwave oven in a fully assembled condition (outer case fitted).

The power output of this oven is rated using the method specified by IEC 60705. Full details of how to curry out this procedure can be found in the

Sharp Technical Training notes which is available from Sharp Parts Centre (part number SERV-LITMW01). The IEC60705 procedure must be carried out using laboratory-type procedures and equipment.

These requirements make the procedure unsuitable for routine performance checks.

NOTE: The following test method gives an indication of the output power only, it cannot be used to establish the actual/rated output power. If the true output power is required, then the IEC60705 test method must be used.

Alternative simplified method:

1.  Place 2 litres of cold water (between 12°C and 20°C) in a suitable container.

2.  Stir the water and measure the temperature in °C. Note temperature as T1.

3.  Place the container in the microwave and heat the water for 1 minute and 48 seconds on full power. NOTE: The operation time of microwave oven includes “3” sec. (3 sec. is magnetron filament heat-up time.)

4.  When the 1 minute and 48 seconds is completed, remove the container and stir the water. Note the water temperature as T2.

5.  Calculate the output power using the following formula: R.F. Power Output = (T2 - T1) x 80.

NOTE: The result from this test should be within the allowance of 2000cc alternative method. (±10%).

2. MICROWAVE LEAKAGE TEST

This oven should be tested for microwave leakage on completion of any repair or adjustment, following the procedure described in the Sharp Techni- cal Training notes (part number SERV-LITMW01). The maximum leakage permitted in BS EN 60335-2-25 is 50W/m2 (equivalent to 5W/m2), however it is not normal to detect any significant leakage, therefore, any leakage which is detected should be investigated.

It is essential that only leakage detectors with current calibration traceable to National Physical Laboratories are used. Suitable leakage detectors: CELTEC A100

APOLLO X1

[2] B: HIGH VOLTAGE TRANSFORMER TEST

WARNING: High voltages and large currents are present at the secondary winding and filament winding of the power transformer. It is very dangerous to work near this part when the oven is on. NEVER make any voltage measurements of the high-voltage cir- cuits, including the magnetron filament.

1.  CARRY OUT 3D CHECKS.

2.  Disconnect the leads to the primary winding of the high voltage transformer. Disconnect the filament and secondary winding co nnections from the rest of the HV circuitry. Using an ohmmeter, set on a low range, it is possible to check the continuity of all three winding. The following readings should be obtained:

a.Primary winding -------------------- 2.6 ohms approximately b.Secondary winding --------------- 199 ohms approximately c.Filament winding ------------------------------ less than 1 ohm

If the readings obtained are not stated as above, then the high voltage transformer is probably faulty and should be replaced.

3.  CARRY OUT 4R CHECKS.

[3] C: HIGH VOLTAGE RECTIFIER TEST

CARRY OUT 3D CHECKS.

Isolate the high voltage rectifier assembly from the HV circuit. The high voltage rectifier can be tested using an ohmmeter set to its highest range. Connect the ohmmeter across the terminal B+C of the high voltage rectifier and note the reading obtained. Reverse the meter leads and note this

second reading. The normal resistance is infinite in one direction and more than 100 kŸ in the other direction.

CARRY OUT 4R CHECKS. ASYMMETRIC RECTIFIER TEST CARRY OUT 3D CHECKS.

Isolate the high voltage rectifier assembly from the HV circuit. The asymmetric rectifier can be tested using an ohmmeter set to its highest range across the terminals A+B of the asymmetric rectifier and note the reading obtained. Reverse the meter leads and note this second reading. If an open circuit is indicated in both directions then the asymmetric rectifier is good. If the

A 	D2	D1	B

ASYMMETRIC

RECTIFIER	HIGH VOLTAGE

C 	RECTIFIER

asymmetric rectifier is shorted in either direction, then the asymmetric rectifier is faulty and must be replaced with high voltage rectifier. When the

asymmetric rectifier is defective, check whether magnetron, high voltage rectifier, high voltage wire or filament winding of the high voltage transformer is shorted.

CARRY OUT 4R CHECKS.

NOTE: FOR MEASUREMENT OF THE RESISTANCE OF THE RECTIFIER, THE BATTERIES OF THE MEASURING INSTRUMENT MUST HAVE A VOLTAGE AT LEAST 6 VOLTS, BECAUSE OTHERWISE AN INFINITE RESISTANCE MIGHT BE SHOWN IN BOTH DIRECTIONS.

[4] D: HIGH VOLTAGE CAPACITOR TEST

CARRY OUT 3D CHECKS.

1.  Isolate the high voltage capacitor from the circuit.

2.  Continuity check must be carried out with measuring instrument which is set to the highest resistance range.

3.  A normal capacitor shows continuity for a short time (kick) and then a resistance of about 10MŸ after it has been charged.

4.  A short-circuited capacitor shows continuity all the time.

5.  An open capacitor constantly shows a resistance about 10 MŸ because of its internal 10MŸ resistance.

6.  When the internal wire is opened in the high voltage capacitor shows an infinite resistance.

7.  The resistance across all the terminals and the chassis must be infinite when the capacitor is normal. If incorrect reading are obtained, the high voltage capacitor must be replaced.

CARRY OUT 4R CHECKS.

[5] E: SWITCH TEST

CARRY OUT 3D CHECKS.

Isolate the switch to be tested and using an ohmmeter check between the terminals as described in the following table.

| Plunger Operation | COM to NO | COM to NC |
| --- | --- | --- |
| Released | Open circuit | Short circuit |
| Depressed | Short circuit | Open circuit. |

| Plunger Operation | COM to NO | COM to NC |
| --- | --- | --- |
| Released | Open circuit | Short circuit |
| Depressed | Short circuit | Open circuit. |

Table: Terminal Connection of Switch

COM; Common terminal

NO;	Normally open terminal

NC;	Normally close terminal

If incorrect readings are obtained, make the necessary switch adjustment or replace the switch. CARRY OUT 4R CHECKS.

[6] F: TEMPERATURE FUSE TEST

CARRY OUT 3D CHECKS.

Disconnect the leads from the terminals of the temperature fuse. Then using an ohmmeter, make a continuity test across the two terminals as described in the below.

Table: Temperature Fuse Test

| Parts Name | Temperature of “ON” condition (closed circuit). | Temperature of “OFF” condition (open circuit). | Indication of ohmmeter (When room temperature is approx. 20°C.) |
| --- | --- | --- | --- |
| Temperature fuse 150°C | This is not resetable type. | Above 150°C | Closed circuit |

If incorrect readings are obtained, replace the temperature fuse.

An open circuit temperature fuse (OVEN) indicates that the food in the oven cavity may catch fire, this may be due to overheating produced by improper setting of the cooking time or failure of the control panel.

CARRY OUT 4R CHECKS.

[7] G: MOTOR WINDING TEST

CARRY OUT 3D CHECKS.

Disconnect the leads from the motor. Using an ohmmeter, check the resistance between the two terminals as described in the table below.

Table: Resistance of Motor

|  | Fan Motors | Turntable motor |
| --- | --- | --- |
| Part Code | RMOTEA405WRZZ | RMOTDA289WRZZ | RMOTDA173WRE0 | RMOTDA253WRZZ |
| Resistance | Approximately 388Ÿ | Approximately 13.5kŸ | Approximately 12.2kŸ | Approximately 14.5kŸ |

If incorrect readings are obtained, replace the motor. CARRY OUT 4R CHECKS.

[8] H: FUSIBLE T6.3A

CARRY OUT 3D CHECKS.

If the fuse T6.3A is blown when the door is opened, check the secondary interlock switch, primary interlock relay (RY2) and monitor switch. If the fuse T6.3A is blown by incorrect door switching replace the defective switch(es) and the fuse T6.3A.

If the fuse T6.3A is blown, there is a shorts or grounds in electrical parts or wire harness. Check them and replace the defective parts or repair the wire harness.

CARRY OUT 4R CHECKS.

CAUTION: ONLY REPLACE FUSE T6.3A WITH THE CORRECT VALUE REPLACEMENT.

[9] I: NOISE FILTER TEST

CARRY OUT 3D CHECKS.

Disconnect the leads from the terminals of the noise filter. Using an ohmmeter, check between the terminals as described in the following table.

NOISE FILTER

N	L

FUSE T6.3A

| MEASURING POINT | INDICATION OF OHMMETER |
| --- | --- |
| Between N and L | Open circuit |
| Between terminal N and WHITE | Short circuit |
| Between terminal L and RED | Short circuit |

| MEASURING POINT | INDICATION OF OHMMETER |
| --- | --- |
| Between N and L | Open circuit |
| Between terminal N and WHITE | Short circuit |
| Between terminal L and RED | Short circuit |

NOISE SUPPRESSION COIL

If incorrect readings are obtained, replace the noise filter unit. CARRY OUT 4R CHECKS.

[10] Procedure J: HIGH VOLTAGE FUSE TEST

CARRY OUT 3D CHECKS.

If the high voltage fuse is blown, there could be a short in the high voltage rectifier or the magnetron. Check them and replace the defective parts and the high voltage fuse. CARRY OUT 4R CHECKS. CAUTION: ONLY REPLACE HIGH VOLTAGE FUSE WITH THE CORRECT VALUE REPLACEMENT

[11] Procedure K: TOUCH CONTROL PANEL ASSEMBLY TEST

WHT

RED

The touch control panel consists of circuits including semiconductors such as LSI, ICs, etc. Therefore, unlike conventional microwave ovens, proper maintenance cannot be performed with only a voltmeter and ohmmeter. In this service manual, the touch control panel assembly is divided into two units, Control Unit and Switch Unit, and also the Control Unit is divided into two units, CPU Unit and Power Unit, and troubleshooting by unit replace- ment is described according to the symptoms indicated.

1.  Switch Unit. Note: Check switch unit wire harness connection before replacement.

The following symptoms indicate a defective switch unit. Replace the switch unit.

1) When touching the buttons, a certain button produces no signal at all.

2) When touching the buttons, sometimes a button produces no signal.

3) When rotating the TIMER/WEIGHT knob, the cooking time or the weight can not be input.

2.  Control Unit.

The following symptoms indicate a defective control unit. Before replacing the switch unit, perform the Switch unit test (Procedure L) to determine if control unit is faulty.

1) In connection with buttons.

a) When touching the buttons, a certain group of buttons do not produce a signal.	b) When touching the buttons, no buttons produce a signal.

2) In connection with indicators.

a) At a certain digit, all or some segments do not light up. b) At a certain digit, brightness is low.

c)  Only one indicator does not light up.

e) Wrong figure appears.

f)  A certain group of indicators do not light up. g) The figure of all digits flicker.

d) The corresponding segments of all digits do not light up; or they continue to light up.

3) Other possible troubles caused by defective control unit. a) Buzzer does not sound or continues to sound.

b) Clock does not operate properly. c)  Cooking is not possible.

[12] Procedure L: SWITCH UNIT TEST

1.  CARRY OUT 3D CHECKS.

2.  Isolate the switch unit with the control panel frame to be tested.

3.  Using an ohmmeter and referring to the switch unit matrix indicated on the switch unit circuit, check the circuit between the pins of the switch unit that correspond to the STOP button. When the button is pressed, the ohmmeter should indicate short circuit. When the button is released, the ohmmeter should indicate open circuit. If incorrect readings are obtained, the switch unitbutton is faulty and must be replaced. About the other but- tons, the above method may be used.

4.  CARRY OUT 4R CHECKS.

(G10)

C   SW100

< SW UNIT>

WH-A

7pin HARNESS

WH-B

4pin HARNESS

WH-C

3pin WIRE HARNESS

H5      A5 (G9)

C-3    A

C-2     B

C-1

(c)

SW6

WHOLE POULTRY

SW5

SW3

ROAST POAK

SW1	SW2

SW9

STOP 	 CEAR

SW8

(G8)    (B4)

(c) (a)

(C100) (C101)

A2	(d)

(b)

(a)

MEAT JOINT

SW7

CHICKEN

AUTO COOK

ROAST BEEF/ LAMB

SW4

ROAST

POWER LEVEL

SW10

START

H6      A6 (G7)

(b)

(R100)

A1

(R101)

QUARTERS

POULITRY

AUTO MINUTE

A4	A3	B3

B2	A7	B1

H4	H3

G6	(G5)

G4	H7(G3)	G2

(H8(G1))

[13] Procedure M: RELAY TEST

CARRY OUT 3D CHECKS.

Remove the outer case and check voltage between the pin No. 3 and No. 5 of connector CN-A on the control unit with an A.C. voltmeter. The meter should indicate 230 - 240 volts, if not check oven circuit.

Relay Test

These relays are operated by D.C. voltage

Check voltage at the relay coil with a D.C. voltmeter during the microwave cooking operation.

DC. voltage indicated ................................... Defective relay.

DC. voltage not indicated ............................. Check diode which is connected to the relay coil. If diode is good, control unit is defective.

| RELAY SYMBOL | OPERATIONAL VOLTAGE | CONNECTED COMPONENTS |
| --- | --- | --- |
| RY5 | Approx. 12.7V D.C. | Oven lamp / Turntable motor / Cooling fan motor |
| RY2 | Approx. 11.7V D.C. | High voltage transformer |
| RY6 | Approx. 12.7V D.C. | Touch control transformer |

CARRY OUT 4R CHECKS.

[14] Procedure N: PROCEDURES TO THE CONTROL UNIT

Problem: POWER ON, indicator does not light up. CARRY OUT 3D CHECKS.

| STEPS | OCCURRENCE | CAUSE OR CORRECTION |
| --- | --- | --- |
| 1 | The rated AC voltage is not present between the Pin No. 3 and Pin No. 5 of connector CN-A. | Check supply voltage and oven power cord. |
| 2 | The oven door is opened and closed. But the rated AC voltage is not present to primary side of low voltage transformer. | Check the secondary interlock switch. If the secondary interlock switch is normal, the fuse or the relay RY-6 is defective. Check and replace the control unit. |
| 3 | The rated AC voltage is present to primary side of low voltage trans- former. | Low voltage transformer or secondary circuit defective. Check and replace the control unit. |

NOTE: At the time of these steps, make a visual inspection of the varistor for burned damage. And examine the transformer with a tester for the pres- ence of layer short-circuit (check the primary coil resistance). If any abnormal condition is detected, replace the control unit.

CARRY OUT 4R CHECKS.

CHAPITRE 9. TOUCH CONTROL PANEL ASSEMBLY

[1] OUTLINE OF TOUCH CONTROL PANEL

The touch control section consists of the following units as shown in the touch control panel circuit.

(1) Switch Unit     (2) Control Unit

The principal functions of these units and their related signals are explained below.

1. Switch Unit

The switch unit is composed of a matrix, signals generated in the LSI are sent to the switch unit through P52, P54, P55 and P56. When a button is pressed, a signal is completed through the switch unit and passed back to the LSI through AN2, AN3 and AN4 to perform the function that was requested. When the jog dial is rotated, the encoder converts the signal from the power source circuit into the pulse signal, and the pulse signal is sent to the LSI through P51 and P46.

2. Control Unit

Control  unit  consists  of  LSI,  reset  circuit,  indicator  circuit,  power source circuit, relay circuit, buzzer circuit and synchronizing signal cir- cuit.

1) Reset Circuit

This circuit generates a signal which resets the LSI to the initial state when power is supplied.

2) Indicator Circuit

This circuit consists of 4-digits, 12-segments and 3-common elec- trodes using a Liquid Crystal Display.

3) Power Source Circuit

This circuit generates voltage necessary in the control unit from the AC line voltage. In addition, the synchronizing signal is available in order to compose a basic standard time in the clock circuit.

| Symbol | Voltage | Application |
| --- | --- | --- |
| VSS | -5V | LSI(IC1) |

4) Relay Circuit

To drive the magnetron, fan motor, turntable motor and light the oven lamp.

5) Buzzer Circuit

The buzzer is responsive to signals from the LSI to emit audible sounds (switch unit touch sound and completion sound).

6) Synchronizing Signal Circuit

The power source synchronizing signal is available in order to com- pose a basic standard time in the clock circuit. It accompanies a very small error because it works on commercial frequency.

7) Door sensing Switch

A switch to “tell” the LSI if the door is open or closed.

8) Back Light Circuit

A circuit to drive the back light (Light emitting diodes LD1 - LD4).

9) Energy Save Mode Circuit

A circuit to drive the touch control transformer. If the oven has not been used for 3 minutes or more, the contacts of the relay RY-6 will be opened and the control unit will not be energized.

[2] SERVICING FOR TOUCH CONTROL PANEL

1. Precautions for Handling Electronic Components

This unit uses CMOS LSI in the integral part of the circuits. When han- dling these parts, the following precautions should be strictly followed. CMOS LSI have extremely high impedance at its input and output ter- minals. For this reason, it is easily influenced by the surrounding high voltage power source, static electricity charge in clothes, etc., and sometimes it is not fully protected by the built-in protection circuit.

In order to protect CMOS LSI.

1) When storing and transporting, thoroughly wrap them in aluminium foil. Also wrap PW boards containing them in aluminium foil.

2) When soldering, ground the technician as shown in the figure and use grounded soldering iron and work table.

approx. 1M ohm

2. Servicing of Touch Control Panel

We describe the procedures to permit servicing of the touch control panel of the microwave oven and the precautions you must take when doing so. To perform the servicing, power to the touch control panel is available either from the power line of the oven itself or from an exter- nal power source.

1.  Servicing the touch control panel with power supply of the oven: CAUTION: THE HIGH VOLTAGE TRANSFORMER OF THE MICRO-

WAVE OVEN IS STILL LIVE DURING SERVICING AND

PRESENTS A HAZARD.

Therefore, before checking the performance of the touch control panel,

1) Disconnect the power supply cord and then remove outer case.

2) Open the door and block it open.

3) Discharge high voltage capacitor.

4) Disconnect the leads to the primary of the power transformer.

5) Ensure that these leads remain isolated from other components and oven chassis by using insulation tape.

6) After that procedure, re-connect the power supply cord. After checking the performance of the touch control panel,

1) Disconnect the power supply cord.

2) Open the door and block it open.

3) Re-connect the leads to the primary of the power transformer.

4) Re-install the outer case (cabinet).

5) Re-connect  the  power  supply  cord  after  the  outer  case  is installed.

6) Run the oven and check all functions.

a) On some models, the power supply cord between the touch control panel and the oven itself is so short that the two can't be separated. For those models, check and repair all the controls (sensor-related ones included) of the touch control panel while keeping it connected to the oven.

b) On some models, the power supply cord between the touch control panel and the oven proper is so long enough that they may be separated from each other. For those models, therefore, it is possible to check and repair the controls of the touch control panel while keeping

it apart from the oven proper; in this case you must short both ends of the door sensing switch (on PWB) of the touch control panel with a jumper, which brings about an opera- tional state that is equivalent to the oven door being closed. As for the sensor-related controls of the touch control panel, checking them is possible if the dummy resistor(s) with resis- tance equal to that of the controls are used.

2.  Servicing the touch control panel with power supply from an exter- nal power source:

Disconnect the touch control panel completely from the oven proper, and short both ends of the door sensing switch (on PWB) of the touch control panel, which brings about an operational state that is equivalent to the oven door being closed. Connect an exter- nal power source to the power input terminal of the touch control panel, then it is possible to check and repair the controls of the touch control panel; it is also possible to check the sensor-related controls of the touch control panel by using the dummy resistor(s).

3. Servicing Tools

Tools required to service the touch control panel assembly.

1) Soldering iron: 60W

(It is recommended to use a soldering iron with a grounding termi- nal.)

2) Oscilloscope: Single beam, frequency range: DC - 10MHz type or more advanced model.

3) Others: Hand tools

4. Other Precautions

1) Before turning on the power source of the control unit, remove the aluminium foil applied for preventing static electricity.

2) Connect the connector of the key unit to the control unit being sure that the lead wires are not twisted.

3) After aluminium foil is removed, be careful that abnormal voltage due to static electricity etc. is not applied to the input or output ter- minals.

4) Attach connectors, electrolytic capacitors, etc. to PWB, making sure that all connections are tight.

5) Be sure to use specified components where high precision is required.

CHAPITRE 10. PRECAUTIONS FOR USING LEAD-FREE SOLDER

1. Employing lead-free solder

The “Main PWB” of this model employs lead-free solder. This is indicated by the “LF” symbol printed on the PWB and in the service manual. The suffix letter indicates the alloy type of the solder.

Example:

Sn-Ag-Ni

Indicates lead-free solder of tin, silver and copper	Indicates lead-free solder of tin, silver and nickle

2. Using lead-free wire solder

When repairing a PWB with the “LF” symbol, only lead-free solder should be used. (Using normal tin/lead alloy solder may result in cold soldered joints and damage to printed patterns.)

As the melting point of lead-free solder is approximately 40°C higher than tin/lead alloy solder, it is recommend that a dedicated bit is used, and that the iron temperature is adjusted accordingly.

3. Soldering

As the melting point of lead-free solder (Sn-Ag-Cu) is higher and has poorer wettability, (flow), to prevent damage to the land of the PWB, extreme care should be taken not to leave the bit in contact with the PWB for an extended period of time. Remove the bit as soon as a good flow is achieved. The high content of tin in lead free solder will cause premature corrosion of the bit. To reduce wear on the bit, reduce the temperature or turn off the iron when it is not required.

Leaving different types of solder on the bit will cause contamination of the different alloys, which will alter their characteristics, making good soldering more difficult. It will be necessary to clean and replace bits more often when using lead-free solder. To reduce bit wear, care should be taken to clean the bit thoroughly after each use.

CHAPITRE 11. COMPONENT	REPLACEMENT	AND	ADJUSTMENT	PROCE- DURE

[1] BEFORE OPERATING

WARNING AGAINST HIGH VOLTAGE:

Microwave ovens contain circuitry capable of producing very high voltage and current, contact with following parts may result in severe, possibly fatal, electric shock.

(Example)

High Voltage Capacitor, High Voltage Transformer, Magnetron, High Voltage Rectifier Assembly, High Voltage Harness High Voltage fuse ,etc.. WARNING: Avoid possible exposure to microwave energy. Please follow the instructions below before operating

the oven.

1) Disconnect the power supply cord.

2) Visually check the door and cavity face plate for damage (dents, cracks, signs of arcing etc.).

Carry out any remedial work that is necessary before operating the oven.

Do not operate the oven if any of the following conditions exist;

1) Door does not close firmly.

2) Door hinge, support or latch hook is damaged.

3) The door gasket or seal is damaged.

4) The door is bent or warped.

5) There are defective parts in the door interlock system.

6) There are defective parts in the microwave generating and trans- mission assembly.

7) There is visible damage to the oven. Do not operate the oven:

1) Without the RF gasket (Magnetron).

2) If the wave guide or oven cavity are not intact.

3) If the door is not closed.

4) If the outer case (cabinet) is not fitted.

WARNING FOR WIRING

To prevent an electric shock, take the following manners.

1.  Before wiring,

1) Disconnect the power supply cord.

2) Open the door and block it open.

3) Discharge the high voltage capacitor and wait for 60 seconds.

2.  Don't let the wire leads touch to the following parts;

1) High voltage parts:

Magnetron, High voltage transformer, High voltage capacitor and High voltage rectifier assembly High voltage fuse.

2) Hot parts:

Oven lamp, Magnetron, High voltage transformer and Oven cavity.

3) Sharp edge:

Bottom plate, Oven cavity, Waveguide flange and other metallic plate.

4) Movable parts (to prevent a fault)

Fan blade, Fan motor, Turntable motor and Switch.

3.  Do not catch the wire leads in the outer case cabinet.

4.  Insert the positive lock connector certainly until its pin is locked and make sure that the wire leads do not come off even if the wire leads are pulled.

5.  To prevent an error function, connect the wire leads correctly, refer- ring to the Pictorial Diagram.

Please refer to ‘OVEN PARTS, CABINET PARTS, CONTROL PANEL PARTS, DOOR PARTS’, when carrying out any of the following removal proce- dures:

REMEMBER TO CHECK 3D

1) Disconnect the supply.	3)Discharge high voltage capacitor.

2)Door opened, and wedged open.

[2] OUTER CASE REMOVAL

To remove the outer case, procedure as follows.

1.  Disconnect the oven from power supply.

2.  Open the oven door and wedge it open.

3.  Remove the two (2) screws from right side of the outer case cabi- net.

4.  Remove the five (5) screws from rear and along the side edge of case.

5.  Slide the entire case back about 3cm to free it from retaining clips on the cavity face plate.

6.  Lift the entire case from the oven.

7.  Discharge the H.V. capacitor before carrying out any further work.

8.  Do not operate the oven with the outer case removed. NOTE: Step 1, 2 and 7 form the basis of the 3D checks.

CAUTION: DISCONNECT OVEN FROM POWER SUPPLY BEFORE REMOVING OUTER CASE.

[3] HIGH VOLTAGE TRANSFORMER REMOVAL

1.  CARRY OUT 3D CHECKS.

2.  Disconnect the wire leads (main wire harness) from high voltage transformer.

3.  Disconnect the filament lead of high voltage transformer from the magnetron.

4.  Disconnect the filament lead of the high voltage transformer from high voltage capacitor.

5.  Disconnect the high voltage wire of the high voltage transformer from the high voltage capacitor.

6.  Remove the four (4) screws holding the transformer to bottom plate from below.

7.  Remove the transformer.

[4] HIGH VOLTAGE RECTIFIER ASSEMBLY, HIGH VOLTAGE FUSE AND HIGH VOLTAGE CAPACITOR REMOVAL

To remove the components, proceed as follows.

1. CARRY OUT 3D CHECKS.

2. Disconnect the H.V. fuse from the high voltage transformer.

3. Disconnect the H.V. wire of the H.V. rectifier assembly from the magnetron.

4. Disconnect the filament lead of the high voltage transformer from the H.V. capacitor.

5. Remove one (1) screw holding capacitor holder to the oven cavity back plate.

5. Remove one (1) screw holding capacitor holder to the oven cavity back plate.

6. Remove one (1) screw holding earth side terminal of high voltage rectifier assembly, and remove capacitor holder.

7. Disconnect all the leads and terminals of high voltage rectifier assembly from high voltage capacitor.

8. Disconnect the H.V. fuse from the high voltage capacitor.

9. Now H.V. rectifier assembly, H.V. fuse and H.V. capacitor should be free.

CAUTION : WHEN REPLACING HIGH VOLTAGE RECTIFIER ASSEMBLY, ENSURE THAT THE CATHODE (EARTH) CONNECTION IS SECURELY FIXED TO THE CAPACITOR HOLDER WITH AN EARTHING SCREW.

CAUTION : DO NOT REPLACE ONLY HIGH VOLTAGE RECTIFIER. WHEN REPLACING IT, REPLACE HIGH VOLTAGE RECTIFIER ASSEMBLY.

[5] MAGNETRON REMOVAL

1. REMOVAL

1.  CARRY OUT 3D  CHECKS.

2.  Disconnect the wire leads from the magnetron.

3.  Remove the two (2) screws holding the air duct to the oven cavity.

4.  Release the air duct from the oven cavity.

5.  Carefully remove the four (4) screws holding the magnetron to the waveguide flange.

6.  Lift up magnetron with care so that the magnetron antenna is not hit by any metal object around antenna.

7.  Now, the magnetron is free.

2. REINSTALLATION

1.  Reinstall the magnetron to the waveguide flange with the four (4)

screws.

2.  Reinstall the air duct to the oven cavity with the two (2) screws.

3.  Reconnect the wire leads to the magnetron. Refer to “PICTORIAL DIAGRAM”.

4.  Reinstall the outer case and check that the oven is operating prop- erly.

CAUTION: WHEN REPLACING THE MAGNETRON, BE SURE THE R.F. GASKET IS IN PLACE AND THE MAGNETRON MOUNTING SCREWS ARE TIGHTENED SECURELY.

[6] POSITIVE LOCK CONNECTOR (NO-CASE TYPE) REMOVAL

1.  CARRY OUT 3D CHECKS.

2.  Push the lever of positive lock   connector.

Terminal

3.  Pull down on the positive lock   connector.

CAUTION: WHEN CONNECTING THE POSITIVE LOCK   CONNEC- TORS TO THE TERMINALS, CONNECT THE POSITIVE LOCK   SO THAT THE LEVER FACES YOU.

Positive lock¨

connector

1

Push

Lever

[7] TURNTABLE MOTOR REMOVAL

1. REMOVAL

1.  Disconnect the power supply cord.

2.  Remove turntable and turntable support from oven cavity.

3.  Lay the oven on it's backside. Remove the turntable motor cover by snipping off the material in four corners.

2

Pull down

Figure C-1. Positive lock, connector

4.  Where the corners have been snipped off bend corner areas flat.

No sharp edges must be evident after removal of the turntable motor cover.

5.  Disconnect wire leads from turntable motor. (See “Positive lock connector removal”)

6.  Remove one (1) screw holding turntable motor to oven cavity.

7.  Remove the TTM packing from the turntable motor.

8.  Now, the turntable motor is free.

2. REINSTALL

1.  Re-install the TTM packing to the turntable motor.

2.  Re-install the turntable motor with the TTM packing with the single

(1) screw to the oven cavity bottom plate.

3.  Re-connect the wire leads to the turntable motor.

4.  Insert the tab of the turntable motor cover into the hole of the bot- tom plate.

5.  Re-install the turntable motor cover to the bottom plate with one (1)

screw.

TTM packing

Turntable motor

Figure C-2. TTM packing Installation

[8] COOLING FAN MOTOR REMOVAL

1. REMOVAL

1.  CARRY OUT 3D  CHECKS.

2.  Disconnect the wire leads from the fan motor.

3.  Remove the two (2) screws holding the fan motor to the oven cavity back plate.

4.  Remove the fan blade from the fan motor shaft according to the fol- lowing procedure.

5.  Hold the edge of the rotor of the fan motor by using a pair of groove joint pliers.

CAUTION: MAKE SURE THAT ANY PIECES DO NOT ENTER THE GAP BETWEEN THE ROTOR AND THE STATOR OF THE FAN MOTOR. BECAUSE THE ROTOR IS EASY TO BE SHAVEN BY PLIERS AND METAL PIECES MAY BE PRO- DUCED.

DO NOT TOUCH THE PLIERS TO THE COIL OF THE FAN MOTOR BECAUSE THE COIL MAY BE CUT OR INJURED.

DO NOT DISFIGURE THE BRACKET BY TOUCHING WITH THE PLIERS.

6.  Remove the fan blade from the shaft of the fan motor by pulling and rotating the fan blade with your hand.

7.  Now, the fan blade will be free.

CAUTION: DO   NOT   RE-USE   THE   REMOVED   FAN   BLADE BECAUSE THE HOLE (FOR SHAFT) MAY BE LARGER THAN NORMAL.

8.  Now, the fan motor is free.

2. INSTALLATION

1.  Install the fan blade to the fan motor shaft according to the following procedure.

2.  Hold the center of the bracket which supports the shaft of the fan motor on the flat table.

3.  Apply the screw lock tight into the hole (for shaft) of the fan blade.

4.  Install the fan blade to the shaft of fan motor by pushing the fan blade with a small, light weight, ball peen hammer or rubber mallet.

CAUTION: DO  NOT  HIT  THE  FAN  BLADE  STRONGLY  WHEN INSTALLED BECAUSE THE BRACKET MAY BE TRANS- FORMED.

MAKE   SURE   THAT   THE   FAN   BLADE   ROTATES SMOOTH AFTER INSTALLED.

MAKE SURE THAT THE AXIS OF THE SHAFT IS NOT SLANTED.

5.  Install the fan motor assembly to the oven cavity back plate with two (2) screws.

6.  Connect the wire leads to the magnetron and fan motor, referring to the pictorial diagram.

Coil

Groove joint pliers

Shaft

Stator Gap Bracket

Rotor

Shaft

Axis

Stator

Rotor

Rear View	Side View

These are the positions that should be pinched with pliers.

Table	Center of bracket

[9] POWER SUPPLY CORD REPLACEMENT

1. REMOVAL

1.  CARRY OUT 3D CHECKS.

2.  Remove the single (1) screw holding the green/yellow wire to the oven cavity back plate.

3.  Disconnect the leads of the power supply cord from the noise filter, referring to the Figure C-3(a).

4.  Release the moulding cord stopper of the power supply cord from

Screw

Green/Yellow

Wire

Power Supply

Cord

L

L

RED

RED

Brown Wire

Oven Cavity

Back Plate

WHT

WHT

the square hole of the oven cavity back plate, referring to the Fig- ure C-3 (b).

Blue

Wire

N

N

Noise Filter

5.  Now, the power supply cord is free.

2. REINSTALL

1.  Insert the moulding cord stopper of power supply cord into the square hole of the rear cabinet, referring to the Figure C-3 (b).

2.  Install the earth wire lead of power supply cord to the oven cavity back plate with one (1) screw and tight the screw.

3.  Connect the brown and blue wire leads of power supply cord to the noise filter correctly, referring to the Pictorial Diagram.

Figure C-3(a) Power Supply Cord Replacement

P ower  S upply

C ord

Moulding

C ord S topper

Oven  C a vity

Ba ck P la te

S qua re

Hole

Figure C-3(a) Figure C-3(b) Power Supply Cord Replacement

[10] CONTROL PANEL ASSEMBLY REMOVAL

1.  CARRY OUT 3D CHECKS.

2.  Disconnect the leads from the control unit.

3.  Remove the one (1) screw holding the control panel to the front panel of the oven cavity.

4.  Lift up the control panel assembly and release it from the oven cav- ity.

5.  Now, the control panel assembly is free.

[11] SECONDARY INTERLOCK SWITCH, DOOR SENSING SWITCH AND MONITOR SWITCH REMOVAL

1. REMOVAL

1.  CARRY OUT 3D CHECKS.

2.  Remove the control panel assembly, referring to section of CON- TROL PANEL ASSEMBLY REMOVAL.

3.  Disconnect wire leads from the switches.

4.  Remove two (2) screws holding latch hook to oven flange.

5.  Remove latch hook assembly from oven flange.

6.  Push outward on the two (2) retaining tabs holding switch in place.

7.  Switch is now free.

2. REINSTALL

1.  Re-install each switch in its place. The secondary interlock switch and the monitor switch are in the lower position and the door sens- ing switch is in the upper position

2.  Secure latch hook (with two (2) mounting screws) to oven flange.

3.  Re-connect wire leads to each switch. Refer to pictorial diagram.

4.  Reinstall the control panel assembly to the oven cavity.

5.  Reconnect wire leads to the control unit, referring to the pictorial diagram.

6.  Make sure that the monitor switch is operating properly and check continuity of the monitor circuit. Refer to chapter “Test Procedure” and Adjustment procedure.

[12] SECONDARY INTERLOCK SWITCH, DOOR SENSING SWITCH AND MONITOR SWITCH ADJUSTMENT

1. Adjustment

1.  CARRY OUT 3D CHECKS.

If the secondary interlock switch, door sensing switch and monitor switch do not operate properly due to a misadjustment, the following adjustment should be made.

2.  Loosen the two (2) screws holding latch hook to the oven cavity front flange.

3.  With door closed, adjust latch hook by moving it back and forth, and up and down. In and out play of the door allowed by the upper and lower position of the latch hook should be less than 0.5mm. The vertical position of the latch hook should be adjusted so that the secondary interlock switch and door sensing switch are acti- vated with the door closed. The horizontal position of the latch hook should be adjusted so that the plunger of the monitor switch is pressed with the door closed.

4.  Secure the screws with washers firmly.

5.  Check the operation of all switches. If each switch has not activated with the door closed, loosen screw and adjust the latch hook posi- tion.

2. After adjustment, check the following.

1. In and out play of door remains less than 0.5mm when in the latched position. First check upper position of latch hook, pushing and pulling upper portion of door toward the oven face.

Then check lower portion of the latch hook, pushing and pulling lower portion of the door toward the oven face. Both results (play in the door) should be less than 0.5mm.

2. When the door is open, the contacts of the secondary interlock switch and door sensing switch open within 1.6mm gap between

right side of cavity face and the door.

Latch Heads

Door

Latch Hook

Door Sensing Switch

Monitor Switch

Secondary interlock Switch

3.  Monitor switch contacts close when door is opened.

4.  Re-install outer case and check for microwave leakage around door with an approved microwave survey meter. (Refer to Micro- wave Measurement Procedure.)

Figure C-5. Latch Switch Adjustments

[13] DOOR REPLACEMENT

1. REMOVAL

1.  Disconnect the power supply cord.

2.  Open the door slightly.

3.  Insert  a  putty  knife  (thickness  of  about  0.5mm)  into  the  gap between the choke cover and corner portion of door panel as shown in Figure C-6 to free engaging parts.

4.  Pry the choke cover by inserting a putty knife as shown Figure C-6.

5.  Release choke cover from door panel.

6.  Now choke cover is free.

NOTE: When carrying out any repair to the door, do not bend or warp the slit choke (tabs on the door panel assembly) to prevent microwave leakage.

Choke Cover

Door Frame

Putty Knife

Figure C-6. Door Disassembly

7.  Release two (2) pins of door panel from two (2) holes of upper and lower oven hinges by lifting up.

8.  Now, door panel with door frame is free from oven cavity.

9.  Remove the two (2) screws holding the door panel to door frame.

10.Release door panel from ten (10) tabs of door frame and remove the door frame by sliding the door panel downward.

11. Now, door panel with sealer film is free.

12.Tear sealer film from door panel.

13.Now, door panel is free.

14.Slide latch head upward and remove it from door frame with releas- ing latch spring from door frame and latch head.

15.Now, latch head and latch spring are free.

16.Remove the two (2) screws holding the door handle and the glass stopper to the door frame.

17.Remove the door handle and the glass stopper from the door frame.

18.Remove theglass stopper from from the dooe frame.

19.Slide the door glass towards the door glass stopper position.

20.Now, door glass is free.

2. REINSTALLATION

1.  Insert door glass into the door frame by reversing the above door glass removing procedure.

2.  Re-install the glass stopper and the door handle to the door frame with the two (2) screws.

3.  Re-install latch spring to the head. Re-install latch spring to the door frame. Re-install latch head to the door frame.

4.  Re-install door panel to door frame by fitting ten (10) tabs of door frame to ten (10) holes of door panel.

5.  Hold the door panel to the door frame with the two (2) screws.

6.  Put sealer film on door panel. Refer to “Sealer Film” about how to handle new one.

7.  Catch two (2) pins of door panel on two (2) hole of upper and lower oven hinges

8.  Re-install choke cover to door panel by pushing. NOTE: After any service to the door;

1) Make sure that secondary interlock switch, door sensing switch and monitor switch are operating properly. (Refer to chapter “Test Procedures”.).

2) An approved microwave survey meter should be used to assure compliance with proper microwave radiation emission limitation standards.

3. After any service, make sure of the following:

1.  Door latch heads smoothly catch latch hook through latch holes and that latch head goes through center of latch hole.

2.  Deviation of door alignment from horizontal line of cavity face plate is to be less than 1.0mm.

3.  Door is positioned with its face pressed toward cavity face plate.

4.  Check for microwave leakage around door with an approved micro- wave survey meter. (Refer to Microwave Measurement Procedure).

NOTE: The door on a microwave oven is designed to act as an electronic seal preventing the leakage of microwave energy from oven cavity during cook cycle. This function does not require that door be air-tight, moisture (conden- sation)-tight or light-tight. Therefore, occasional appear- ance of moisture, light or sensing of gentle warm air movement around oven door is not abnormal and do not of themselves, indicate a leakage of microwave energy from oven cavity.

4. SEALER FILM

1.  Put the adhesive tape on the backing film of the sealer film as shown in Fig. C-8

2.  Tear the backing film by pulling the adhesive tape.

3.  Put the pasted side of the sealer film on the door panel

Sealer film 	Backing film

Adhesive tape

Pin

Upper

Oven Hinge

Upper Oven

Hinge

Figure C-8. Sealer film

Slit choke of door panel

Lower

Oven Hinge

Lower Oven

Hinge

Pin

Choke Cover

Figure C-7. Door Replacement

CHAPITRE 12. MICROWAVE MEASUREMENT

After any repair, the microwave oven must be checked for microwave leakage to ensure continued safe operation. BS EN 60335-2-25 specifies that the maximum permitted leakage with a load of 275 ml is 50 W/m2 (equivalent to 5 mW/cm2) at a distance of 5 cm from the oven.

PREPARATION

The following items are required to carry out this test:

1.  A low form of 600 ml beaker made from an electrically non-conductive material, such as glass or plastic, with an inside diameter of approximately

8.5 cm. This must contain 275 ± 15 ml of water, at an initial temperature of 20 ± 2°C.

2.  A leakage detector which has been calibrated within the preceding 12 months to a stand whose accuracy can be traced to National Physical Lab- oratory Standards.

Recommended instruments are:- Apollo “XI”

Celtec “A100”

Before commencing the test, check that the leakage detector is functioning and adjusted according to the manufacturer's instructions, and any spac- ers are fitted to ensure that measurement is taken 5cm from the surface of the oven.

PROCEDURE

3.  Place the beaker containing the water load in the oven cavity at the centre of the turntable. The placing of this standard load in the oven is impor- tant, not only to protect the oven, but also to ensure that any leakage it is not disguised by too large a load absorbing energy.

4.  2.Close the oven door, and with the power level set to FULL, turn the oven ON with the timer set for a few minutes operation. Should the water begin to boil before the test has been completed, it should be replaced.

5.  3.As shown in the diagram below, move the probe slowly (not faster than 2.5 cm/sec.);-

1) around the edge of the door following the gap

2) across the face of the door

3) across any vents in the oven's sides, rear or top

Dotted line indicates the path taken by the leakage detector.

Whilst the maximum leakage permitted in BS EN 60335-2-25 is 50 W/m2 (equivalent to 5 mW/cm2), it is not normal to detect any si	gnificant leakage, and therefore any detected leakage should be investigated.

CHAPITRE 13. CIRCUIT DIAGRAMS

[1] Oven Schematic

SCHEMATIC NOTE: CONDITION OF OVEN

1. DOOR CLOSED.

2. PLUGGED IN OVEN

3. NOTHING APEARS ON DISPLAY.

L

L

TEMP FUSE

NOTE: "   " indicates components with potentials above 250V

FUSE  T6.3A

FUSE  T6.3A

MAGNETRON

LINE  BYPASS CAPACITOR

0.0022uF / AC 250V

LINE  BYPASS CAPACITOR

0.0022uF / AC 250V

A5	A7

CONTROL UNIT

HIGH VOLTAGE TRANSFORMER

LINE  CROSS CAPACITOR

0.068uF / AC 250V

LINE  CROSS CAPACITOR

0.068uF / AC 250V

NOISE SUPPRESSION COIL

NOISE SUPPRESSION COIL

H.V. FUSE

0.6 A

H.V. FUSE

0.6 A

FUSE 2.5A

GRN

(RY-6)

(RY-5)

(RY-2) PRIMARY INTERLOCK RELAY

OVEN LAMP

OL

TURN TABLE MOTOR

TTM

MONITOR SWITCH

LINE  BYPASS CAPACITOR

0.0022uF / AC 250V

LINE  BYPASS CAPACITOR

0.0022uF / AC 250V

A3	A1	B1	B3

DOOR SENSING SWITCH

FM

FAN MOTOR

N.C.

N

N

COM.

N.O. SECONDARY

INTERLOCK

SWITCH

Figure O-1(a) Oven Schematic-OFF Condition right after the oven is plugged in.

SCHEMATIC

NOTE: CONDITION OF OVEN

1. PLUGGED IN OVEN.

2. DOOR OPENED.

3. “ . 0” APPEARS ON DISPLAY.

L

L

TEMP FUSE

FUSE T6.3A

FUSE T6.3A

MAGNETRON

LINE BYPASS CAPACITOR

0.0022uF / AC 250V

LINE BYPASS CAPACITOR

0.0022uF / AC 250V

A5	A7

CONTROL UNIT

HIGH VOLTAGE TRANSFORMER

LINE CROSS CAPACITOR

0.068uF / AC 250V

LINE CROSS CAPACITOR

0.068uF / AC 250V

NOISE SUPPRESSION COIL

NOISE SUPPRESSION COIL

H.V. FUSE

0.6 A

H.V. FUSE

0.6 A

FUSE 2.5A

GRN

(RY-6)

(RY-5)

(RY-2)   PRIMARY INTERLOCK RELAY

OVEN LAMP

OL

TURN TABLE MOTOR

TTM

H.V. CAPACITOR

0.9uF 2100V AC

H.V. CAPACITOR

0.9uF 2100V AC

MONITOR SWITCH

LINE BYPASS CAPACITOR

0.0022uF / AC 250V

LINE BYPASS CAPACITOR

0.0022uF / AC 250V

A3	A1	B1	B3

DOOR SENSING SWITCH

FM

FAN MOTOR

N.C.

N

N

COM.

N.O. SECONDARY

INTERLOCK

SWITCH

H.V. RECTIFIER

H.V. RECTIFIER

H.V. RECTIFIER

H.V. RECTIFIER

Figure O-1(b) Oven Schematic-OFF Condition when the oven door is opened.

SCHEMATIC

NOTE: CONDITION OF OVEN

1. DOOR CLOSED.

2. PLUGGED IN OVEN.

3. DOOR OPENED AND CLOSED.

4. “ . 0” APPEARS ON DISPLAY.

L

L

TEMP FUSE

NOTE: "    " indicates components with potentials above 250V

FUSE T6.3A

FUSE T6.3A

MAGNETRON

LINE BYPASS CAPACITOR

0.0022uF / AC 250V

LINE BYPASS CAPACITOR

0.0022uF / AC 250V

A5	A7

CONTROL UNIT

HIGH VOLTAGE TRANSFORMER

LINE CROSS CAPACITOR

0.068uF / AC 250V

LINE CROSS CAPACITOR

0.068uF / AC 250V

NOISE SUPPRESSION COIL

NOISE SUPPRESSION COIL

H.V. FUSE

0.6 A

H.V. FUSE

0.6 A

FUSE 2.5A

GRN

(RY-6)

(RY-5)

(RY-2)   PRIMARY INTERLOCK RELAY

OVEN LAMP

OL

TURN TABLE MOTOR

TTM

H.V. CAPACITOR

0.9uF 2100V AC

H.V. CAPACITOR

0.9uF 2100V AC

H.V. RECTIFIER

H.V. RECTIFIER

MONITOR SWITCH

LINE BYPASS CAPACITOR

0.0022uF / AC 250V

LINE BYPASS CAPACITOR

0.0022uF / AC 250V

A3	A1	B1	B3

DOOR SENSING SWITCH

FM

FAN MOTOR

N.C.

N

N

COM.

N.O. SECONDARY

INTERLOCK

SWITCH

Figure O-1(C) Oven Schematic-OFF Condition when the oven door is closed.

SCHEMATIC NOTE: CONDITION OF OVEN

1. DOOR CLOSED.

2. COOKING TIME PROGRAMMED.

3. START BUTTON PRESSED.

L

L

TEMP FUSE

FUSE T6.3A

FUSE T6.3A

MAGNETRON

LINE  BYPASS CAPACITOR

0.0022uF / AC 250V

LINE  BYPASS CAPACITOR

0.0022uF / AC 250V

A5	A7

CONTROL UNIT

HIGH VOLTAGE TRANSFORMER

LINE  CROSS CAPACITOR

0.068uF / AC 250V

LINE  CROSS CAPACITOR

0.068uF / AC 250V

NOISE SUPPRESSION COIL

NOISE SUPPRESSION COIL

H.V. FUSE

0.6 A

H.V. FUSE

0.6 A

FUSE 2.5A

GRN

(RY-6)

(RY-5)

(RY-2) PRIMARY INTERLOCK RELAY

OVEN LAMP

OL

TURN TABLE MOTOR

TTM

H.V. CAPACITOR

0.9uF 2100V AC

H.V. CAPACITOR

0.9uF 2100V AC

H.V. RECTIFIER

H.V. RECTIFIER

MONITOR SWITCH

LINE  BYPASS CAPACITOR

0.0022uF / AC 250V

LINE  BYPASS CAPACITOR

0.0022uF / AC 250V

A3	A1	B1	B3

DOOR SENSING SWITCH

FM

FAN MOTOR

N.C.

N

N

COM.

N.O. SECONDARY

INTERLOCK

SWITCH

Figure O-2 Oven Schematic-ON Condition

CONTROL PANEL

GRN GRN

DOOR SENSING SWITCH

N.O.

GRN

TEMPERATURE FUSE (OVEN)

Screw

G

/ Y

Power Supply

Cord	Oven Cavity

Cord	Oven Cavity

Back Plate

RED

RED

F1: FUSE LIVE

L

L

WHT

WHT

BRN

RED

(SWITCH UNIT)

WH-A

WH-B

(POWER UNIT)

CN-G

3

3

CN-H

CN-B

3 GRN

2

1 GRY

COM

GRY

RED

ORG

BLU

NEUTRAL

N

N

WHT WHT

Noise Filter

BLK RED

ORG ORG

CN-B

RY2

CN-A

7 BLK

6

5 ORG

4

3 WHT

2

1 GRY

BLK

WHT

1

1

RED ORG

WHT

OVEN LAMP

FAN MOTOR

WHT ORG

CN-A

7	1

MONITOR SWITCH

N.C.

GRY

HIGH VOLTAGE COMPONENTS

COM

MAGNETRON

R-27ST

[2] Pictorial Diagram (Figure S-1)

R-27ST

[2] Pictorial Diagram (Figure S-1)

Figure S-1. Pictorial Diagram

Figure S-1. Pictorial Diagram

13 – 3

13 – 3

SECONDARY INTERLOCK SWITCH

COM

N.C.

WHT WHT

GRY

GRY BLU

TURNTABLE MOTOR

WHT BLK

RED

RED WHT

BLU

HIGH VOLTAGE FUSE

HIGH VOLTAGE CAPACITOR

H.V. RECTIFIER HIGH VOLTAGE

TRANSFORMER

T1

VRS1

VRS1

470V

470V

ZD1

HZ12B-1

ZD1

HZ12B-1

D3	D1 D1~D4 1N4002X4

INT

H1

GND

CN-H B7B-PH-K-S(LF)(SN)

(C63)

(G10)

C   SW100

< SW UNIT>

WH-A

7pin HARNESS

WH-B

4pin HARNESS

WH-C

3pin WIRE HARNESS

2.5A

2.5A

D4     D2

Q3	Q2

R6

1K

R6

1K

C5

ZD3

ZD3

UDZS4.3B

UDZS4.3B

0.1uF

(C62)

H5      A5 (G9)

C4

C4

0.01uF

25V

0.01uF

25V

C-3   AB

C-2

C-1

(c)

SW6

WHOLE POULTRY

SW5

SW3

ROAST POAK

SW1	SW2

SW9

STOP 	 CEAR

SW8

CN-A

C6

C6

AC    A5

+	Q1

0.1uF/50V

1000uF/25V

0.1uF/50V

1000uF/25V

2SB1238

R1

390

R1

390

-

R2

F1

F1

C1

C1

C2

C2

R3

1/2W 510     H2

+

C3

C3

10uF/35V

10uF/35V

-

(d)

R7

10K

R7

10K

-5V

50V

2SA1162

(C61)

(C60)

(ZD2)

HZ5C2

(ZD2)

HZ5C2

(G8)    (B4)

0.01uF / 25V

0.01uF / 25V

H6      A6 (G7)

(c) (a)

(b)

(C100) (C101) (R100)

(R101)

(b)

A2           (d)

(a)

R8

1K

R8

1K

A1

MEAT JOINT

SW7

CHICKEN QUARTERS

AUTO COOK

ROAST BEEF/ LAMB

SW4

ROAST POULITRY

POWER LEVEL

SW10

START AUTO MINUTE

R5	LD1 LD2 LD3  LD4	Q4

A4	A3	B3

B2	A7	B1

SE    A1

AC230V~240V

50HZ

AC    A3

OL TTM FM      A7

D27

D27

RY6	J2

FTR-F3AA012E	J3

D26

D26

RY5

FTR-F3AA012E

1/4W 200

R9

R9

10K

10K

(LD5) R30

3.3K

R50

100K R51

100K R67

R66

R65 (R64) R63

R62

R61 (R60)

10K x8

R50

100K R51

100K R67

R66

R65 (R64) R63

R62

R61 (R60)

10K x8

SP1

BL

BZ

SE

OL TTM FM

(R10)

Q30

Q27

Q26

CN-G B03B-XASK-1(LF)(SN)

CN-G B03B-XASK-1(LF)(SN)

(R75) R74 (R73)

R72

100K x3

H4

C51

0.01uF / 25V C52

0.01uF / 25V (R71)

R70 (R69) R68

10K x3

H3	G6

(G5)

G4	H7(G3)	G2

(H8(G1))

(COM)

C7

C7

(Q25)

R76

1M

R76

1M

R11

4.7K

R11

4.7K

CF1

4MHz

(CN- C)

(C1) (C2)

INVERTER

Q21

RN1401

C21

-

+ 10uF/35V

0.1uF / 16V

0.1uF / 16V

(R20)

PWM

DB (BoH)

Q20

(Q28)

C20

0.1uF

16V (Q24)

P37

P60

VCC VCC XOUT XIN VSS P61

P62

RESET

OSCSEL P40

P41

AN2

AN3

AN4

AN5

P37

P60

VCC VCC XOUT XIN VSS P61

P62

RESET

OSCSEL P40

P41

AN2

AN3

AN4

AN5

17	1

MICRO

B3

RY2

DU12D1-1P(M)-R-S

J5

J5

Q31

RN1401

R40

4.7K

R40

4.7K

C40

C40

0.01uF

25V

0.01uF

25V

D20

(ToH)

M

R41

(Q23)

Q22

18

T2OUT P35

P34

P33

P32

P31

P30

COM3

COM2

D22

D22

IC-1

65

P46

P47

VREF AVSS INT0

P51

P52

P53

P54

DOOR SW.

B1	DOOR

CN-B

< POWER UNIT >

10K

COM1

COM0

VL3

SEG23

SEG22

SEG21

Base Pattern: VSS(-5V)

P55

P56

P57

SEG0

SEG1

SEG2

SEG3

VSS VPP RESET ESDA ESCLK ESPGMB VCC

VSS VPP RESET ESDA ESCLK ESPGMB VCC

SEG20

SEG19

SEG18

SEG17

SEG16

SEG15

SEG14

SEG13

SEG12

SEG11

SEG10

SEG9

SEG8

SEG7

SEG6

SEG5

SEG4

SEG20

SEG19

SEG18

SEG17

SEG16

SEG15

SEG14

SEG13

SEG12

SEG11

SEG10

SEG9

SEG8

SEG7

SEG6

SEG5

SEG4

32	50

NOTE: IF NOT SPECIFIED

1/10W +5%,-5%

1SS133 or 1SS270A

33

* Checker land 7 point

C1

C2

C3

C1

C2

C3

( for Q'z ROM writing )

49

< LSI UNIT >

S1

S2

S3

S4

S5

S6

S7

S8

S9

S10

S11

S12 (S13) (S14)

S1

S2

S3

S4

S5

S6

S7

S8

S9

S10

S11

S12 (S13) (S14)

DTA143EAK or KRA101S or RN2401

R-27ST

R-27ST

[3] Control Unit Circuit (Figure S-2)

[3] Control Unit Circuit (Figure S-2)

Figure S-2. Control Unit Circuit

Figure S-2. Control Unit Circuit

13 – 4

13 – 4

(    ) NOT INSERTED PARTS

LCD

[4] Printed Wiring Board

Figure S-3. Printed Wiring Board of Power Unit	Figure S-4. Printed Wiring Board of Switchr Unit

13 – 5

GUIDE PIECES

HOW TO ORDER REPLACEMENT PARTS To have your order filled promptly and correctly, please furnish the following information.

1. MODEL NUMBER

2. REF. NO.

3. PART NO.

4. DESCRIPTION

MODELE

MICROWAVE OVEN

R-27ST

Parts marked "*" may cause undue microwave exposure.

Parts marked "	" are used in voltage more than 250V.

[1]	OVEN PARTS

CONTENTS

PARTS

[2]	DOOR AND CONTROL PANEL

INDEX

TOP PAD ASSEMBLY

FPADBA713WRKZ

6-7 CAUTION LABEL

DOOR PROTECTION SHEET SPADPA580WRE0

POLYETHYLENG BAG SSAKHA014WRE0

6-4 INSTRUCTION BOOK

6-1  TURNTABLE TRAY

MICROWAVE OVEN

BOTTOM PAD ASSEMBLY

FPADBA714WRKZ

INTO THE OVEN CAVITY

6-2 TURNTABLE SUPPORT

TRAY PAD ASSY (CPADBA287WRKZ)

Not replaceable items.

PACKING CASE SPAKCF318WREZ

This document has been published to be used for after sales service only.

The contents are subject to change without notice.

[1] OVEN PARTS

7-8

2-1

7-9

7-8

7-8

7-9

4-6

7-6

7-8

7-8

4-9

1-9

7-8

4-11

1-13

7-1

1-1

1-5

7-1

7-8

7-8

7-6

1-3

4-8

4-5

7-2

7-6

7-7

7-7

4-7

4-4

4-13

6-1

6-2

4-10

7-1

4-17

2-2

7-1

1-14

1-12

7-4

7-5

4-16

4-1

1-2

1-8

1-10

1-11	7-3

1-6

4-2

4-3

1-7

4-14

4-12

7-1

1-4

7-8

1-15

2-3

7-8

7-9

7-8

7-10

2-3

7-10

7-7

7-9

4-15

| NO. | PARTS CODE | PRICE RANK | NEW MARK | PART RANK | DESCRIPTION |
| --- | --- | --- | --- | --- | --- |
| [1] OVEN PART |
| ELECTRIC PARTS |
| 1-1 | QACC-A172WRZZ | AS |  |  | Power supply cord |
| 1-2 | FH-DZA165WRKZ | AK |  |  | High voltage rectifier assembly |
| 1-3 | FPWBFA387WRKZ | AW |  |  | Noise filter |
| 1-3 | FPWBFA347WRKZ | AX |  |  | Noise filter (Interchangable) |
| 1-4 | RC-QZA218WRE0 | AW |  |  | High voltage capacitor |
| 1-4 | RC-QZA295WRZZ | AV |  |  | High voltage capacitor (Interchangable) |
| 1-4 | RC-QZA333WRZZ | AS |  |  | High voltage capacitor (Interchangable) |
| 1-5 | QFS-CA027WRZZ | AG |  |  | Fuse T6.3A |
| 1-6 | QSW-MA170WRZZ | AK |  |  | Secondary interlock switch |
| 1-6 | QSW-MA139WRZZ | AQ |  |  | Secondary interlock switch (Interchangable) |
| 1-6 | QSW-MA146WRZZ | AM |  |  | Secondary interlock switch (Interchangable) |
| 1-6 | QSW-MA087WRE0 | AF |  |  | Secondary interlock switch (Interchangable) |
| 1-7 | RMOTEA450WRZZ | AV |  |  | Fan motor |
| 1-7 | RMOTEA405WRZZ | AX |  |  | Fan motor (Interchangable) |
| 1-7 | RMOTEA460WRZZ | AX |  |  | Fan motor (Interchangable) |
| 1-7 | RMOTEA463WRZZ | AX |  |  | Fan motor (Interchangable) |
| 1-7 | RMOTEA475WRZZ | AX |  |  | Fan motor (Interchangable) |
| 1-8 | RV-MZA351WRZZ | BM |  |  | Magnetron |
| 1-8 | RV-MZA341WRZZ | BG |  |  | Magnetron (Interchangable) |
| 1-8 | RV-MZA382WRZZ | BD |  |  | Magnetron (Interchangable) |
| 1-9 | RLMPTA088WRZZ | AN |  |  | Oven lamp |
| 1-9 | RLMPTA083WRZZ | AM |  |  | Oven lamp (Interchangable) |
| 1-9 | RLMPTA101WRZZ | AM |  |  | Oven lamp (Interchangable) |
| 1-10 | QSW-MA168WRZZ | AK |  |  | Door sensing switch |
| 1-10 | QSW-MA147WRZZ | AG |  |  | Door sensing switch (Interchangable) |
| 1-10 | QSW-MA085WRE0 | AF |  |  | Door sensing switch (Interchangable) |
| 1-11 | QSW-MA169WRZZ | AF |  |  | Monitor switch |
| 1-11 | QSW-MA148WRZZ | AF |  |  | Monitor switch (Interchangable) |
| 1-11 | QSW-MA138WRZZ | AH |  |  | Monitor switch (Interchangable) |
| 1-11 | QSW-MA086WRE0 | AF |  |  | Monitor switch (Interchangable) |
| 1-12 | RTRN-A806WRZZ | BF |  |  | High voltage transformer |
| 1-12 | RTRN-A759WRZZ | BH |  |  | High voltage transformer (Interchangable) |
| 1-13 | QFS-TA014WRE0 | AG |  |  | Temperature fuse 150 C (Oven) |
| 1-14 | RMOTDA289WRZZ | AQ |  |  | Turntable motor |
| 1-14 | RMOTDA302WRZZ | AN |  |  | Turntable motor (Interchangable) |
| 1-14 | RMOTDA173WRE0 | AR |  |  | Turntable motor (Interchangable) |
| 1-14 | RMOTDA299WRZZ | AN |  |  | Turntable motor (Interchangable) |
| 1-14 | RMOTDA253WRZZ | AN |  |  | Turntable motor (Interchangable) |
| 1-15 | QFS-IA016WRZZ | AN |  |  | High voltage fuse |
| CABINET PARTS |
| 2-1 | GCABUA995WRPZ | BE |  |  | Outer case cabinet |
| 2-2 | GDAI-A459WRWZ | AF |  |  | Bottom plate |
| 2-3 | GLEGPA104WREZ | AF |  |  | Foot |
| OVEN PARTS |
| 4-1 | PHOK-A146WRFZ | AG |  |  | Latch hook |
| 4-2 | LBNDKA168WRPZ2 | AF |  |  | Capacitor holder |
| 4-3 | NFANJA053WRFZ | AG |  |  | Fan blade |
| 4-4 | PDUC-A908WRWZ2 | AG |  |  | Fan duct |
| 4-5 | FOVN-A634WRTZ | BC |  |  | Oven cavity |
| 4-6 | LANGFA267WRPZ2 | AF |  |  | Chassis support |
| 4-7 | PSPAJA007WRFZ | AF |  |  | Spacer |
| 4-8 | PCOVPA419WREZ | AG |  |  | Waveguide cover |
| 4-9 | PDUC-A909WRPZ | AN |  |  | Air duct |
| 4-10 | PPACGA084WRF0 | AF |  |  | TTM packing |
| 4-11 | PCUSUA501WRP0 | AB |  |  | Cushion |
| 4-12 | PPACGA276WREZ | AG |  |  | Cushion |
| 4-13 | PCUSGA615WRPZ | AE |  |  | Cushion |
| 4-14 | PCUSGA661WREZ | AD |  |  | Cushion A |
| 4-15 | PCUSUA278WRP0 | AB |  |  | Cushion |
| 4-16 | PCUSUA647WRPZ | AC |  |  | Cushion |
| 4-17 | PCUSGA833WRPZ | AC |  |  | Cushion |
| MISCELLANEOUS |
| 6-1 | NTNT-A034WRF0 | AM |  |  | Turntable |
| 6-2 | FROLPA113WRKZ | AS |  |  | Turntable support |
| SCREWS, NUTS AND WASHERS |
| 7-1 | XHPS740P08K00 | AB |  |  | Screw : 4mm x 8mm |
| 7-2 | XETS740P10000 | AA |  |  | Screw : 4mm x 10mm |
| 7-3 | XHPS740P08000 | AB |  |  | Screw : 4mm x 8mm |
| 7-4 | LX-CZ0052WRE0 | AA |  |  | Special screw |
| 7-5 | XOTS740P12000 | AA |  |  | Screw : 4mm x 12mm |
| 7-6 | LX-CZA073WRE0 | AC |  |  | Special screw |
| 7-7 | XHTS740P08RV0 | AG |  |  | Screw : 4mm x 8mm |
| 7-8 | XOTS740P08000 | AA |  |  | Screw : 4mm x 8mm |
| 7-9 | XOTS740P12RV0 | AD |  |  | Screw : 4mm x 12mm |
| 7-10 | LX-BZA217WREZ | AD |  |  | Special screw |

| NO. | PARTS CODE | PRICE RANK | NEW MARK | PART RANK | DESCRIPTION |
| --- | --- | --- | --- | --- | --- |
| [1] OVEN PART |
| ELECTRIC PARTS |
| 1-1 | QACC-A172WRZZ | AS |  |  | Power supply cord |
| 1-2 | FH-DZA165WRKZ | AK |  |  | High voltage rectifier assembly |
| 1-3 | FPWBFA387WRKZ | AW |  |  | Noise filter |
| 1-3 | FPWBFA347WRKZ | AX |  |  | Noise filter (Interchangable) |
| 1-4 | RC-QZA218WRE0 | AW |  |  | High voltage capacitor |
| 1-4 | RC-QZA295WRZZ | AV |  |  | High voltage capacitor (Interchangable) |
| 1-4 | RC-QZA333WRZZ | AS |  |  | High voltage capacitor (Interchangable) |
| 1-5 | QFS-CA027WRZZ | AG |  |  | Fuse T6.3A |
| 1-6 | QSW-MA170WRZZ | AK |  |  | Secondary interlock switch |
| 1-6 | QSW-MA139WRZZ | AQ |  |  | Secondary interlock switch (Interchangable) |
| 1-6 | QSW-MA146WRZZ | AM |  |  | Secondary interlock switch (Interchangable) |
| 1-6 | QSW-MA087WRE0 | AF |  |  | Secondary interlock switch (Interchangable) |
| 1-7 | RMOTEA450WRZZ | AV |  |  | Fan motor |
| 1-7 | RMOTEA405WRZZ | AX |  |  | Fan motor (Interchangable) |
| 1-7 | RMOTEA460WRZZ | AX |  |  | Fan motor (Interchangable) |
| 1-7 | RMOTEA463WRZZ | AX |  |  | Fan motor (Interchangable) |
| 1-7 | RMOTEA475WRZZ | AX |  |  | Fan motor (Interchangable) |
| 1-8 | RV-MZA351WRZZ | BM |  |  | Magnetron |
| 1-8 | RV-MZA341WRZZ | BG |  |  | Magnetron (Interchangable) |
| 1-8 | RV-MZA382WRZZ | BD |  |  | Magnetron (Interchangable) |
| 1-9 | RLMPTA088WRZZ | AN |  |  | Oven lamp |
| 1-9 | RLMPTA083WRZZ | AM |  |  | Oven lamp (Interchangable) |
| 1-9 | RLMPTA101WRZZ | AM |  |  | Oven lamp (Interchangable) |
| 1-10 | QSW-MA168WRZZ | AK |  |  | Door sensing switch |
| 1-10 | QSW-MA147WRZZ | AG |  |  | Door sensing switch (Interchangable) |
| 1-10 | QSW-MA085WRE0 | AF |  |  | Door sensing switch (Interchangable) |
| 1-11 | QSW-MA169WRZZ | AF |  |  | Monitor switch |
| 1-11 | QSW-MA148WRZZ | AF |  |  | Monitor switch (Interchangable) |
| 1-11 | QSW-MA138WRZZ | AH |  |  | Monitor switch (Interchangable) |
| 1-11 | QSW-MA086WRE0 | AF |  |  | Monitor switch (Interchangable) |
| 1-12 | RTRN-A806WRZZ | BF |  |  | High voltage transformer |
| 1-12 | RTRN-A759WRZZ | BH |  |  | High voltage transformer (Interchangable) |
| 1-13 | QFS-TA014WRE0 | AG |  |  | Temperature fuse 150 C (Oven) |
| 1-14 | RMOTDA289WRZZ | AQ |  |  | Turntable motor |
| 1-14 | RMOTDA302WRZZ | AN |  |  | Turntable motor (Interchangable) |
| 1-14 | RMOTDA173WRE0 | AR |  |  | Turntable motor (Interchangable) |
| 1-14 | RMOTDA299WRZZ | AN |  |  | Turntable motor (Interchangable) |
| 1-14 | RMOTDA253WRZZ | AN |  |  | Turntable motor (Interchangable) |
| 1-15 | QFS-IA016WRZZ | AN |  |  | High voltage fuse |
| CABINET PARTS |
| 2-1 | GCABUA995WRPZ | BE |  |  | Outer case cabinet |
| 2-2 | GDAI-A459WRWZ | AF |  |  | Bottom plate |
| 2-3 | GLEGPA104WREZ | AF |  |  | Foot |
| OVEN PARTS |
| 4-1 | PHOK-A146WRFZ | AG |  |  | Latch hook |
| 4-2 | LBNDKA168WRPZ2 | AF |  |  | Capacitor holder |
| 4-3 | NFANJA053WRFZ | AG |  |  | Fan blade |
| 4-4 | PDUC-A908WRWZ2 | AG |  |  | Fan duct |
| 4-5 | FOVN-A634WRTZ | BC |  |  | Oven cavity |
| 4-6 | LANGFA267WRPZ2 | AF |  |  | Chassis support |
| 4-7 | PSPAJA007WRFZ | AF |  |  | Spacer |
| 4-8 | PCOVPA419WREZ | AG |  |  | Waveguide cover |
| 4-9 | PDUC-A909WRPZ | AN |  |  | Air duct |
| 4-10 | PPACGA084WRF0 | AF |  |  | TTM packing |
| 4-11 | PCUSUA501WRP0 | AB |  |  | Cushion |
| 4-12 | PPACGA276WREZ | AG |  |  | Cushion |
| 4-13 | PCUSGA615WRPZ | AE |  |  | Cushion |
| 4-14 | PCUSGA661WREZ | AD |  |  | Cushion A |
| 4-15 | PCUSUA278WRP0 | AB |  |  | Cushion |
| 4-16 | PCUSUA647WRPZ | AC |  |  | Cushion |
| 4-17 | PCUSGA833WRPZ | AC |  |  | Cushion |
| MISCELLANEOUS |
| 6-1 | NTNT-A034WRF0 | AM |  |  | Turntable |
| 6-2 | FROLPA113WRKZ | AS |  |  | Turntable support |
| SCREWS, NUTS AND WASHERS |
| 7-1 | XHPS740P08K00 | AB |  |  | Screw : 4mm x 8mm |
| 7-2 | XETS740P10000 | AA |  |  | Screw : 4mm x 10mm |
| 7-3 | XHPS740P08000 | AB |  |  | Screw : 4mm x 8mm |
| 7-4 | LX-CZ0052WRE0 | AA |  |  | Special screw |
| 7-5 | XOTS740P12000 | AA |  |  | Screw : 4mm x 12mm |
| 7-6 | LX-CZA073WRE0 | AC |  |  | Special screw |
| 7-7 | XHTS740P08RV0 | AG |  |  | Screw : 4mm x 8mm |
| 7-8 | XOTS740P08000 | AA |  |  | Screw : 4mm x 8mm |
| 7-9 | XOTS740P12RV0 | AD |  |  | Screw : 4mm x 12mm |
| 7-10 | LX-BZA217WREZ | AD |  |  | Special screw |

*

*

*

*

*

[2] DOOR AND CONTROL PANEL PARTS

5-11

5-10

5-1

5-2

5-14

5-13

5-9

5-12

5-8

5-6

5-14

3-9

5-3

5-12

3-10

3-1

3-10

5-4

5-5

5-7

3-3

3-11

3-6

3-2

3-10

3-10

3-10

6-4

6-7

3-8

6-5

3-4

6-6

| NO. | PARTS CODE | PRICE RANK | NEW MARK | PART RANK | DESCRIPTION |
| --- | --- | --- | --- | --- | --- |
| [2] DOOR AND CONTROL PANEL PARTS |
| CONTROL PANEL PARTS |
| 3-1 | DPWB-B157DRKZ | BE |  |  | Control unit |
| 3-2 | DPWB-A804DRKZ | BM |  |  | Switch unit |
| 3-3 | FPNLCC117WRKZ | BA |  |  | Panel sub assy |
| 3-6 | JBTN-B515WRTZ | AH |  |  | Key button A |
| 3-8 | JKNBKA764WRTZ | AM |  |  | Timer knob |
| 3-9 | PCUSUA173WRP0 | AC |  |  | Cushion |
| 3-10 | XEPS730P08XS0 | AB |  |  | Screw ; 3mm x 8mm |
| 3-11 | MSPRCA169WREZ | AC |  |  | Earth spring |
| DOOR PARTS |
| 5-1 | FDORFA397WRTZ | BB |  |  | Door panel assembly |
| 5-2 | GWAKPB248WRTZ | AY |  |  | Door frame |
| 5-3 | HDECQA392WRRZ | AN |  |  | Door decoration A |
| 5-4 | HDECQA393WRPZ | AH |  |  | Door decoration B |
| 5-5 | JHNDMA063WRTZ | AQ |  |  | Door handle |
| 5-6 | LSTPPA211WRFZ | AG |  |  | Latch head |
| 5-7 | LSTPPA291WRFZ | AH |  |  | Glass stopper |
| 5-8 | MSPRTA187WRE0 | AC |  |  | Spring |
| 5-9 | PGLSPA754WREZ | AR |  |  | Door glass |
| 5-10 | PSHEPA782WREZ | AG |  |  | Sealer film |
| 5-11 | GCOVHA424WRFZ | AK |  |  | Choke cover |
| 5-12 | XEPS730P10XS0 | AA |  |  | Screw : 3m x 10mm |
| 5-13 | HDECQA391WRFZ | AG |  |  | Door sash |
| 5-14 | XEPS740P08000 | AB |  |  | Screw : 4m x 8mm |
| MISCELLANEOUS |
| 6-4 | TINSZA255WRRZ | AM |  |  | Instruction book |
| 6-5 | FW-VZC236WREZ | AP |  |  | Main wire harness |
| 6-6 | FW-VZC262WREZ | AE |  |  | Switch harness |
| 6-7 | TCAUHA349WRRZ | AA |  |  | Caution label |

| NO. | PARTS CODE | PRICE RANK | NEW MARK | PART RANK | DESCRIPTION |
| --- | --- | --- | --- | --- | --- |
| [2] DOOR AND CONTROL PANEL PARTS |
| CONTROL PANEL PARTS |
| 3-1 | DPWB-B157DRKZ | BE |  |  | Control unit |
| 3-2 | DPWB-A804DRKZ | BM |  |  | Switch unit |
| 3-3 | FPNLCC117WRKZ | BA |  |  | Panel sub assy |
| 3-6 | JBTN-B515WRTZ | AH |  |  | Key button A |
| 3-8 | JKNBKA764WRTZ | AM |  |  | Timer knob |
| 3-9 | PCUSUA173WRP0 | AC |  |  | Cushion |
| 3-10 | XEPS730P08XS0 | AB |  |  | Screw ; 3mm x 8mm |
| 3-11 | MSPRCA169WREZ | AC |  |  | Earth spring |
| DOOR PARTS |
| 5-1 | FDORFA397WRTZ | BB |  |  | Door panel assembly |
| 5-2 | GWAKPB248WRTZ | AY |  |  | Door frame |
| 5-3 | HDECQA392WRRZ | AN |  |  | Door decoration A |
| 5-4 | HDECQA393WRPZ | AH |  |  | Door decoration B |
| 5-5 | JHNDMA063WRTZ | AQ |  |  | Door handle |
| 5-6 | LSTPPA211WRFZ | AG |  |  | Latch head |
| 5-7 | LSTPPA291WRFZ | AH |  |  | Glass stopper |
| 5-8 | MSPRTA187WRE0 | AC |  |  | Spring |
| 5-9 | PGLSPA754WREZ | AR |  |  | Door glass |
| 5-10 | PSHEPA782WREZ | AG |  |  | Sealer film |
| 5-11 | GCOVHA424WRFZ | AK |  |  | Choke cover |
| 5-12 | XEPS730P10XS0 | AA |  |  | Screw : 3m x 10mm |
| 5-13 | HDECQA391WRFZ | AG |  |  | Door sash |
| 5-14 | XEPS740P08000 | AB |  |  | Screw : 4m x 8mm |
| MISCELLANEOUS |
| 6-4 | TINSZA255WRRZ | AM |  |  | Instruction book |
| 6-5 | FW-VZC236WREZ | AP |  |  | Main wire harness |
| 6-6 | FW-VZC262WREZ | AE |  |  | Switch harness |
| 6-7 | TCAUHA349WRRZ | AA |  |  | Caution label |

*

*

*

*

COPYRIGHT © 2009 BY SHARP CORPORATION ALL RIGHTS RESERVED.

No part of this publication may be reproduced, stored in retrieval systems, or transmitted in any form or by any means, electronic, mechanical, photocopying, re- cording, or other wise, without prior written permission of the publisher.